## Slide 1: Perspective Projection
CS 543 / ECE 549 http://saurabhg.web.illinois.edu/teaching/ece549/sp2021/
Many slides adapted from S. Seitz, L. Lazebnik, B. Hariharan.
Video source: Camera Obscura & World of Illusions

## Slide 2: Overview of next two lectures
The pinhole projection model
  Geometric properties
  Perspective projection matrix
Cameras with lenses
  Depth of focus
  Field of view
  Lens aberrations
Digital sensors

## Slide 3: Let’s design a camera
Idea 1: put a piece of film in front of an object
Do we get a reasonable image?
Slide by Steve Seitz

## Slide 4: Pinhole camera
Add a barrier to block off most of the rays
Slide by Steve Seitz
Notes: It gets inverted

## Slide 5: Pinhole camera
Captures pencil of rays – all rays through a single point: aperture, center of projection, optical center, focal point, camera center
The image is formed on the image plane
Slide by Steve Seitz

## Slide 6: Pinhole cameras are everywhere
Tree shadow during a solar eclipse
photo credit: Nils van der Burg http://www.physicstogo.org/index.cfm
Slide by Steve Seitz

## Slide 7: Camera obscura
Basic principle known to Mozi (470-390 BCE), Aristotle (384-322 BCE)
Drawing aid for artists: described by Leonardo da Vinci (1452-1519)
Gemma Frisius, 1558
Image source
Slide by L. Lazebnik.

## Slide 8: Turning a room into a camera obscura
Abelardo Morell, Camera Obscura Image of Manhattan View Looking South in Large Room, 1996
http://www.abelardomorell.net/project/camera-obscura/
From Grand Images Through a Tiny Opening, Photo District News, February 2005

## Slide 9: Turning a room into a camera obscura
Camera Obscura: View of Central Park Looking West in Bedroom. Summer, 2018
http://www.abelardomorell.net/project/camera-obscura/
From Grand Images Through a Tiny Opening, Photo District News, February 2005
Adapted from L. Lazebnik.

## Slide 10: Turning a room into a camera obscura
A. Torralba and W. Freeman, Accidental Pinhole and Pinspeck Cameras, CVPR 2012
Slide by L. Lazebnik.

## Slide 11: Pinhole projection model
To compute the projection p of a scene point P, form the visual ray connecting P to the camera center O and find where it intersects the image plane
P
O
p
Slide by L. Lazebnik.

## Slide 12: Pinhole projection model
The coordinate system
  The optical center (O) is at the origin
  The image plane is parallel to xy-plane or perpendicular to the z-axis, which is the optical axis
P
O
p
z
x
y
Slide by L. Lazebnik.

## Slide 13: Pinhole projection model
f
Z
P
y
O
p
Projection equations
  Derived using similar triangles
Y
Note: instead of dealing with an image that is upside down, most of the time we will pretend that the image plane is in front of the camera center.
Slide by L. Lazebnik.
= (x, y)

## Slide 14: Dimensionality reduction: from 3D to 2D
Figures © Stephen E. Palmer, 2002
3D world
2D image
What properties of the world are preserved?
  Straight Lines
  Angles
  Incidence
  Lengths
  Parallel Lines
Slide by A. Efros

## Slide 15: Dimensionality reduction: from 3D to 2D
Figures © Stephen E. Palmer, 2002
3D world
2D image
What properties of the world are preserved?
  Straight lines, incidence
What properties are not preserved?
  Angles, lengths
Slide by A. Efros

## Slide 16: Properties of projection
Which is closer?
Who is taller?
Slide by Derek Hoiem

## Slide 17: Properties of projection
Perpendicular?
Parallel?
Slide by Derek Hoiem

## Slide 18
Vanishing Point

## Slide 19: Vanishing points

## Slide 20: Parallel lines converge at a point
Line L1:
Line L2:
Point Pi
.
Adapted from B. Hariharan.

## Slide 21: Parallel lines converge at a point
Study, behavior of as ,
which is same as .
But, what happens if ?
Adapted from B. Hariharan.

## Slide 22: Parallel lines converge at a point
lines?
Adapted from B. Hariharan.

## Slide 23: Farther away objects are smaller
Foot:
Image of foot:
Image of head:
Head:
Height:
Adapted from B. Hariharan.

## Slide 24: What about planes?
As ,
Planes vanish into a line.
Parallel planes vanish into the same line.
Plane:
Plane:
Adapted from B. Hariharan.

## Slide 25: Except?
and .
Fronto-parallel plane.

## Slide 26: Fronto-parallel planes
What happens to the projection of a pattern on a plane parallel to the image plane?
  All points on that plane are at a fixed depth z
  The pattern gets scaled by a factor of f / z, but angles and ratios of lengths/areas are preserved
Slide from L. Lazebnik

## Slide 27: Vanishing points
All parallel lines converge to a vanishing point
  Each direction in space is associated with its own vanishing point
  Exception: directions parallel to the image plane

## Slide 28: Constructing the vanishing point of a line
image plane
camera
center
line in the scene
vanishing point
Slide by Steve Seitz
Notes: If we have another line in the scene parallel to the first one, it will have the same vanishing point

## Slide 29: Vanishing lines of planes
Image source
  How do we construct the vanishing line of a plane?
Notes: Is this parachutist higher or lower than the person taking this picture?
Lower—he is below the horizon

## Slide 30: Horizon: Vanishing line of ground plane
camera
Ground plane

## Slide 31: Vanishing lines of planes
Image source: S. Seitz
  Is the parachutist above or below the camera?
Notes: Is this parachutist higher or lower than the person taking this picture?
Lower—he is below the horizon

## Slide 32: Comparing heights
Vanishing
Point
Slide by Steve Seitz

## Slide 33: Measuring height
1
2
3
4
5
5.4
2.8
3.3
Camera height
What is the height of the camera?
Slide by Steve Seitz

## Slide 34: Horizon: Vanishing line of ground plane
Adapted from Steve Seitz
  Horizon: vanishing line of the ground plane
    All points at the same height as the camera project to the horizon
    Points higher (resp. lower) than the camera project above (resp. below) the horizon
    Provides way of comparing height of objects
camera
Ground plane

## Slide 35: Horizon: Vanishing line of ground plane
camera
Ground plane
camera
Ground plane

## Slide 36: Vanishing lines of planes
Slide by Steve Seitz
camera
center
plane in the scene
  Horizon: vanishing line of the ground plane
    All points at the same height as the camera project to the horizon
    Points higher (resp. lower) than the camera project above (resp. below) the horizon
    Provides way of comparing height of objects

## Slide 37: Fun with Projective Geometry
Illusion Credit: RN Shepard, Mind Sights: Original Visual Illusions, Ambiguities, and other Anomalies

## Slide 38: Perspective cues
Slide by Steve Seitz

## Slide 39: Perspective cues in art
Masaccio, Trinity, Santa Maria Novella, Florence, 1425-28
One of the first consistent uses of perspective in Western art
Slide from L. Lazebnik

## Slide 40: Perspective distortion
What is the shape of the projection of a sphere?
Image source: F. Durand

## Slide 41: Perspective distortion
Are the widths of the projected columns equal?
  The exterior columns are wider
  This is not an optical illusion, and is not due to lens flaws
  Phenomenon pointed out by Da Vinci
Source: F. Durand

## Slide 42: Perspective distortion: People
Slide from L. Lazebnik

## Slide 43: Modeling projection
Projection equation:
Source: J. Ponce, S. Seitz
x
y
z
f
Note: instead of dealing with an image that is upside down, most of the time we will pretend that the image plane is in front of the camera center.
= (x, y)
Notes: The camera projection scales the apparent height of objects by the inverse of the depth. This results in the well-known effect that objects farther away from the camera look smaller.
We don’t care that the image is upside down: we can simply pretend that the image plane is in front of the camera center.

## Slide 44: Homogeneous coordinates
Is this a linear transformation?
Trick: add one more coordinate:
homogeneous image
coordinates
homogeneous scene
coordinates
Converting from homogeneous coordinates
  no—division by z is nonlinear
Slide by Steve Seitz

## Slide 45: Perspective Projection Matrix
divide by the third coordinate
Projection is a matrix multiplication using homogeneous coordinates
In practice: lots of coordinate transformations…
World to camera coord. trans. matrix (4x4)
Perspective projection matrix (3x4)
Camera to pixel coord. trans. matrix (3x3)
=
2D
point (3x1)
3D point (4x1)
Slide from L. Lazebnik

## Slide 46: Orthographic Projection
Special case of perspective projection
  Distance from center of projection to image plane is infinite
  Also called “parallel projection”
Image
World
Slide by Steve Seitz
Notes: Is this a linear function?

## Slide 47: Orthographic Projection
Special case of perspective projection
  Distance from center of projection to image plane is infinite
  Also called “parallel projection”
Slide from L. Lazebnik
Notes: Is this a linear function?

## Slide 48: Orthographic Projection
Special case of perspective projection
  Distance from center of projection to image plane is infinite
  Also called “parallel projection”
  What’s the projection matrix?
Image
World
Slide by Steve Seitz
Notes: Is this a linear function?

## Slide 49: Recap
f
Z
P
y
O
p
Y
Notes: It gets inverted