## Slide 1: Light, Camera and Shading
CS 543 / ECE 549 – Saurabh Gupta
Spring 2021, UIUC
http://saurabhg.web.illinois.edu/teaching/ece549/sp2020/
Many slides adapted from S. Seitz, L. Lazebnik, D. Hoiem, D. Forsyth

## Slide 2: Recap
Notes: It gets inverted

## Slide 3: Recap
Notes: It gets inverted

## Slide 4: Recap
Notes: Review slide (skip)

## Slide 5: Overview
Cameras with lenses
  Depth of field
  Field of view
  Lens aberrations
Brightness of a pixel
  Small taste of radiometry
  In-camera transformation of light
  Reflectance properties of surfaces
  Lambertian reflection model
  Shape from shading

## Slide 6: Building a Real Camera

## Slide 7: Home-made pinhole camera
http://www.debevec.org/Pinhole/
Slide by A. Efros

## Slide 8: Shrinking the aperture
Why not make the aperture as small as possible?
  Less light gets through
  Diffraction effects…
Slide by Steve Seitz

## Slide 9: Shrinking the aperture
Slide by Steve Seitz

## Slide 10: Adding a lens

## Slide 11: Adding a lens
A lens focuses light onto the film
  Thin lens model:
    Rays passing through the center are not deviated (pinhole projection model still holds)
Slide by Steve Seitz

## Slide 12: Adding a lens
A lens focuses light onto the film
  Thin lens model:
    Rays passing through the center are not deviated (pinhole projection model still holds)
    All rays parallel to the optical axis pass through the focal point
    All parallel rays converge to points on the focal plane
Slide by Steve Seitz
focal point
f

## Slide 13: Thin lens formula
Where does the lens focus the rays coming from a given point in the scene?
f
Slide by Frédo Durand
object
image plane
lens
Notes: This is the relation between the focal length (f), the distance of the object from the camera (D), and the distance at which the object will be in focus (D’)

## Slide 14: Thin lens formula
What is the relation between the focal length ( f ), the distance of the object from the optical center (D), and the distance at which the object will be in focus (D′)?
f
D
D′
Slide by Frédo Durand
object
image plane
lens
Notes: This is the relation between the focal length (f), the distance of the object from the camera (D), and the distance at which the object will be in focus (D’)

## Slide 15: Thin lens formula
f
D
D′
Similar triangles everywhere!
Slide by Frédo Durand
object
image plane
lens

## Slide 16: Thin lens formula
f
D
D′
Similar triangles everywhere!
y′
y
y′/y = D′/D
Slide by Frédo Durand
object
image plane
lens

## Slide 17: Thin lens formula
f
D
D′
Similar triangles everywhere!
y′
y
y′/y = (D′−f )/f
Slide by Frédo Durand
object
image plane
lens
y′/y = D′/D

## Slide 18: Thin lens formula
f
D
D′
1
D′
D
1
1
f
+
=
Any point satisfying the thin lens equation is in focus.
Slide by Frédo Durand
object
image plane
lens
What happens when D is very large?
Notes: And the set of all such points forms a plane parallel to the image (plane of focus).
Uses of the formula: given focal length and depth in scene that you want to be in focus, it tells you where to put the image plane. Given f and distance of image plane from camera center, it tells you which depth in the scene will be in focus.

## Slide 19: Depth of Field
For a fixed focal length, there is a specific distance at which objects are “in focus”
  Other points project to a “circle of confusion” in the image
“circle of
confusion”
Slide by Steve Seitz

## Slide 20: Depth of Field
http://www.cambridgeincolour.com/tutorials/depth-of-field.htm
Slide by A. Efros
Notes: Depth of field is the distance between the nearest and farthest objects in a scene that appear acceptably sharp in an image (Wikipedia)

## Slide 21: Controlling depth of field
http://en.wikipedia.org/wiki/File:Depth_of_field_illustration.svg
Changing the aperture size affects depth of field
  A smaller aperture increases the range in which the object is approximately in focus
  But small aperture reduces amount of light – need to increase exposure

## Slide 22: Varying the aperture
Large aperture = small DOF
Small aperture = large DOF
Slide by A. Efros

## Slide 23: Field of View
f
Larger focal length = smaller FOV
Slide by A. Efros
FOV depends on focal length and size of the camera retina

## Slide 24: Field of View
Slide by A. Efros
Notes: The field of view is the angular extent of the world that is observed by the camera.

## Slide 25: Field of View
Slide by A. Efros

## Slide 26: Field of View / Focal Length
Large FOV, small f
Camera close to car
Small FOV, large f
Camera far from the car
Sources: A. Efros, F. Durand

## Slide 27: Same effect for faces
standard
wide-angle
telephoto
Source: F. Durand

## Slide 28: Approximating an orthographic camera
Source: Hartley & Zisserman

## Slide 29: The dolly zoom
Continuously adjusting the focal length while the camera moves away from (or towards) the subject
http://en.wikipedia.org/wiki/Dolly_zoom

## Slide 30: The dolly zoom
Continuously adjusting the focal length while the camera moves away from (or towards) the subject
“The Vertigo shot”
Example of dolly zoom from Goodfellas (YouTube)
Example of dolly zoom from La Haine (YouTube)

## Slide 31: Real lenses

## Slide 32: Lens flaws: Vignetting

## Slide 33: Radial Distortion
No distortion
Pin cushion
Barrel
  Caused by imperfect lenses
  Deviations are most noticeable near the edge of the lens

## Slide 34: Lens flaws: Spherical aberration
Spherical lenses don’t focus light perfectly
Rays farther from the optical axis focus closer

## Slide 35: Lens Flaws: Chromatic Aberration
Lens has different refractive indices for different wavelengths: causes color fringing
Near Lens Center
Near Lens Outer Edge

## Slide 36: Lens Flaws: Chromatic Aberration
Researchers tried teaching a network about objects by forcing it to assemble jigsaws.
Slide Credit: C. Doersch

## Slide 37: Digital camera sensors
Each cell in a sensor array is a light-sensitive diode that converts photons to electrons
  Dominant in the past: Charge Coupled Device (CCD)
  Dominant now: Complementary Metal Oxide Semiconductor (CMOS)
http://electronics360.globalspec.com/article/9464/ccd-vs-cmos-the-shift-in-image-sensor-technology

## Slide 38: Rolling Shutter
Rolling Shutter: pixels read in sequence
Can get global reading, but $$$

## Slide 39: Overview
Cameras with lenses
  Depth of field
  Field of view
  Lens aberrations
Brightness of a pixel
  Small taste of radiometry
  In-camera transformation of light
  Reflectance properties of surfaces
  Lambertian reflection model
  Shape from shading

## Slide 40: Image formation
What determines the brightness of an image pixel?
Distribution and properties of light sources
Surface shape and orientation
Surface reflectance properties
Optics
Sensor properties
Slide by L. Fei-Fei
Exposure
Notes: Review slide (skip)

## Slide 41: Fundamental radiometric relation
L: Radiance emitted from P toward P’
  Energy carried by a ray (Watts per sq. meter per steradian)
E: Irradiance falling on P’ from the lens
  Energy arriving at a surface (Watts per sq. meter)
What is the relationship between E and L?
Szeliski 2.2.3
P
P’
f
z
d
α
Notes: Radiance: energy carried by a ray (light coming from a source)
• Measure of the density of photons passing near P and traveling in a small cone of directions towards P’.
• Power per unit area perpendicular to the direction of travel, per unit solid angle
• Units: Watts per square meter per steradian
Irradiance: energy arriving at a surface
• Incident power per unit area (not foreshortened)
• Units: Watts per square meter

## Slide 42: Fundamental radiometric relation
Image irradiance is linearly related to scene radiance
Irradiance is proportional to the area of the lens and inversely proportional to the squared distance between the lens and the image plane
The irradiance falls off as the angle between the viewing ray and the optical axis increases
Szeliski 2.2.3
P
P’
f
z
d
α
Notes: Difference between the cos^4 alpha effect and mechanical vignetting: the former effect has nothing to do with light getting lost in the lens system but is a basic radiometric property even of a perfect lens; mechanical vignetting is usually much stronger.

## Slide 43
Relation between Image Irradiance E and Scene Radiance L
f
z
surface patch
image plane
image patch
Solid angles of the double cone (orange and green):
(1)
Solid angle subtended by lens:
(2)
Slide from S Narasimhan.

## Slide 44
Relation between Image Irradiance E and Scene Radiance L
f
z
surface patch
image plane
image patch
Flux received by lens from = Flux projected onto image
(3)
From (1), (2), and (3):
Image irradiance is proportional to Scene Radiance!
Small field of view  Effects of 4th power of cosine are small.
Slide from
S Narasimhan.

## Slide 45: Fundamental radiometric relation
S. B. Kang and R. Weiss. Can we calibrate a camera using an image of a flat, textureless Lambertian surface? ECCV 2000
Notes: The brightest point corresponds to the principal point (where the optical axis intersects the image plane). The shape of the curves of constant brightness tells us about the shape (scaling factors) of the pixels. The equation also includes the focal length (z’). Thus, we can in principle figure out all the intrinsic camera parameters using the constraints given by this equation (fundamental radiometric relation).

## Slide 46: From light rays to pixel values
Camera response function: the mapping f from irradiance to pixel values
  Useful if we want to estimate material properties
  Enables us to create high dynamic range (HDR) images
  Classic reference: P. E. Debevec and J. Malik, Recovering High Dynamic Range Radiance Maps from Photographs, SIGGRAPH 97

## Slide 47
The Problem of Dynamic Range
Dynamic Range: Range of brightness values measurable with a camera
(Hood 1986)
High Exposure Image
Low Exposure Image
We need 5-10 million values to store all brightnesses around us.
But, typical 8-bit cameras provide only 256 values!!
Today’s Cameras: Limited Dynamic Range
Slide from S Narasimhan.

## Slide 48
Images taken with a fish-eye lens of the sky show the wide range of brightnesses.
High Dynamic Range Imaging
Capture a lot of images with different exposure settings.
Apply radiometric calibration to each camera.
Combine the calibrated images (for example, using averaging weighted by exposures).
(Debevec)
(Mitsunaga)
Slide from S Narasimhan.

## Slide 49: Basic models of reflection
Specular: light bounces off at the incident angle
  E.g., mirror
Diffuse: light scatters in all directions
  E.g., brick, cloth, rough wood
incoming light
specular reflection
incoming light
diffuse reflection
Slide from D. Hoiem

## Slide 50: Other possible effects
light source
transparency
light source
refraction
Slide from D. Hoiem

## Slide 51: Other possible effects
λ
light source
subsurface scattering
https://en.wikipedia.org/wiki/Subsurface_scattering#/media/File:Skin_Subsurface_Scattering.jpg
Slide from D. Hoiem

## Slide 52: Other possible effects
λ1
light source
λ2
fluorescence
t=1
light source
t>1
phosphorescence
https://en.wikipedia.org/wiki/Fluorescence#/media/File:Fluorescent_minerals_hg.jpg
Slide from D. Hoiem

## Slide 53: Overview
Cameras with lenses
  Depth of field
  Field of view
  Lens aberrations
Brightness of a pixel
  Small taste of radiometry
  In-camera transformation of light
  Reflectance properties of surfaces
  Lambertian reflection model
  Shape from shading

## Slide 54: Lambertian reflectance model
Some light is absorbed (function of albedo)
Remaining light is scattered (diffuse reflection)
Examples: soft cloth, concrete, matte paints
light source
light source
absorption
diffuse reflection
Slide from D. Hoiem
Notes: albedo is the fraction of light reflected

## Slide 55
Diffuse reflection: Lambert’s cosine law
Intensity does not depend on viewer angle.
  Amount of reflected light proportional to
  Visible solid angle also proportional to
http://en.wikipedia.org/wiki/Lambert%27s_cosine_law
Slide from D. Hoiem

## Slide 56: Recap
When light hits a typical surface
  Some light is absorbed (1-)
    More absorbed for low albedos
  Some light is reflected diffusely
    Independent of viewing direction
  Some light is reflected specularly
    Light bounces off (like a mirror), depends on viewing direction
specular reflection
diffuse reflection
absorption
Slide from D. Hoiem

## Slide 57: Specular Reflection
Reflected direction depends on light orientation and surface normal
  E.g., mirrors are fully specular
  Most surfaces can be modeled with a mixture of diffuse and specular components
light source
specular reflection
Flickr, by suzysputnik
Flickr, by piratejohnny
Slide from D. Hoiem

## Slide 58: Most surfaces have both specular and diffuse components
Specularity = spot where specular reflection dominates (typically reflects light source)
Photo: northcountryhardwoodfloors.com
Typically, specular component is small
Slide from D. Hoiem

## Slide 59: Intensity and Surface Orientation
Intensity depends on illumination angle because less light comes in at oblique angles.
albedo
directional source
surface normal
reflected intensity
Slide: Forsyth

## Slide 60: The interaction of light and surfaces
What happens when a light ray hits a point on an object?
  Some of the light gets absorbed
    converted to other forms of energy (e.g., heat)
  Some gets transmitted through the object
    possibly bent, through refraction
    or scattered inside the object (subsurface scattering)
  Some gets reflected
    possibly in multiple directions at once
  Really complicated things can happen
    fluorescence
Bidirectional reflectance distribution function (BRDF)
  How bright a surface appears when viewed from one direction when light falls on it from another
  Definition: ratio of the radiance in the emitted direction to irradiance in the incident direction
Source: Steve Seitz

## Slide 61: BRDF: Bidirectional Reflectance Distribution Function
surface normal
Slide credit: S. Savarese
Model of local reflection that tells how bright a surface appears when viewed from one direction when light falls on it from another

## Slide 62: BRDFs can be incredibly complicated…

## Slide 63: Diffuse reflection
Light is reflected equally in all directions
  Dull, matte surfaces like chalk or latex paint
  Microfacets scatter incoming light randomly
Brightness of the surface depends on the incidence of illumination
brighter
darker

## Slide 64: Diffuse reflection: Lambert’s law
N
S
B: radiosity (total power leaving the surface per unit area)
ρ: albedo (fraction of incident irradiance reflected by the surface)
N: unit normal
S: source vector (magnitude proportional to intensity of the source)
θ
Slide from L. Lazebnik
Notes: BRDF is constant
  Albedo: fraction of incident irradiance reflected by the surface
  Radiosity: total power leaving the surface per unit area (regardless of direction)

## Slide 65: Specular reflection
Radiation arriving along a source direction leaves along the specular direction (source direction reflected about normal)
On real surfaces, energy usually goes into a lobe of directions
Phong model: reflected energy falls of with
Moving the light source
Changing the exponent
Slide from L. Lazebnik

## Slide 66: Specular reflection
Picture source
Slide from L. Lazebnik

## Slide 67: Photometric stereo (shape from shading)
Can we reconstruct the shape of an object based on shading cues?
Luca della Robbia, Cantoria, 1438
Slide from L. Lazebnik

## Slide 68: Photometric stereo
Assume:
  A Lambertian object
  A local shading model (each point on a surface receives light only from sources visible at that point)
  A set of known light source directions
  A set of pictures of an object, obtained in exactly the same camera/object configuration but using different sources
  Orthographic projection
Goal: reconstruct object shape and albedo
Sn
???
S1
S2
F&P 2nd ed., sec. 2.2.4
Slide from L. Lazebnik

## Slide 69: Example 1
Recovered albedo
Recovered normal field
F&P 2nd ed., sec. 2.2.4
Recovered surface model
Slide from L. Lazebnik

## Slide 70: Example 2
…
Input
Recovered albedo
Recovered normal field
x
y
z
Recovered surface model
Slide from L. Lazebnik

## Slide 71: Image model
Known: source vectors Sj and pixel values Ij(x,y)
Unknown: surface normal N(x,y) and albedo ρ(x,y)
F&P 2nd ed., sec. 2.2.4
Slide from L. Lazebnik

## Slide 72: Image model
Known: source vectors Sj and pixel values Ij(x,y)
Unknown: surface normal N(x,y) and albedo ρ(x,y)
Assume that the response function of the camera is a linear scaling by a factor of k
Lambert’s law:
F&P 2nd ed., sec. 2.2.4
Slide from L. Lazebnik

## Slide 73: Least squares problem
Obtain least-squares solution for g(x,y) (which we defined as N(x,y)  (x,y))
Since N(x,y) is the unit normal,  (x,y) is given by the magnitude of g(x,y)
Finally, N(x,y) = g(x,y) /  (x,y)
(n × 1)
known
known
unknown
(n × 3)
(3 × 1)
For each pixel, set up a linear system:
F&P 2nd ed., sec. 2.2.4
Slide from L. Lazebnik

## Slide 74: Synthetic example
Recovered albedo
Recovered normal field
F&P 2nd ed., sec. 2.2.4
Slide from L. Lazebnik

## Slide 75: Recovering a surface from normals
Recall the surface is written as
This means the normal has the form:
If we write the estimated vector g as
Then we obtain values for the partial derivatives of the surface:
F&P 2nd ed., sec. 2.2.4
Slide from L. Lazebnik

## Slide 76: Recovering a surface from normals
Integrability: for the surface f to exist, the mixed second partial derivatives must be equal:
We can now recover the surface height at any point by integration along some path, e.g.
(for robustness, should take integrals over many different paths and average the results)
(in practice, they should at least be similar)
F&P 2nd ed., sec. 2.2.4
Slide from L. Lazebnik

## Slide 77: Surface recovered by integration
F&P 2nd ed., sec. 2.2.4
Slide from L. Lazebnik

## Slide 78: Limitations
Orthographic camera model
Simplistic reflectance and lighting model
No shadows
No interreflections
No missing data
Integration is tricky
Slide from L. Lazebnik

## Slide 79: Finding the direction of the light source
I(x,y) = N(x,y) ·S(x,y)
Full 3D case:
P. Nillius and J.-O. Eklundh, “Automatic estimation of the projected light source direction,” CVPR 2001
N
S
Notes: We assume the object has uniform albedo, which gets “rolled into” the magnitude of the light source term

## Slide 80: Finding the direction of the light source
Consider points on the occluding contour:
P. Nillius and J.-O. Eklundh, “Automatic estimation of the projected light source direction,” CVPR 2001
Image
Projection direction (z)
Nz positive
Nz = 0
Nz negative
Notes: We assume the object has uniform albedo, which gets “rolled into” the magnitude of the light source term

## Slide 81: Finding the direction of the light source
I(x,y) = N(x,y) ·S(x,y)
Full 3D case:
For points on the occluding contour, Nz = 0:
P. Nillius and J.-O. Eklundh, “Automatic estimation of the projected light source direction,” CVPR 2001
N
S
Notes: We assume the object has uniform albedo, which gets “rolled into” the magnitude of the light source term

## Slide 82: Finding the direction of the light source
P. Nillius and J.-O. Eklundh, “Automatic estimation of the projected light source direction,” CVPR 2001

## Slide 83: Application: Detecting composite photos
Fake photo
Real photo
M. K. Johnson and H. Farid, Exposing Digital Forgeries by Detecting Inconsistencies in Lighting, ACM Multimedia and Security Workshop, 2005.