## Slide 1: Geometry of a single camera
Slides from Derek Hoiem, Svetlana Lazebnik

## Slide 2: Our goal: Recovery of 3D structure
J. Vermeer, Music Lesson, 1662
A. Criminisi, M. Kemp, and A. Zisserman,Bringing Pictorial Space to Life: computer techniques for the analysis of paintings, Proc. Computers and the History of Art, 2002

## Slide 3: Things aren’t always as they appear…
http://en.wikipedia.org/wiki/Ames_room

## Slide 4: Single-view ambiguity
x
X?
X?
X?

## Slide 5: Single-view ambiguity

## Slide 6: Single-view ambiguity
Rashad Alakbarov shadow sculptures

## Slide 7: Anamorphic perspective
Image source

## Slide 8: Our goal: Recovery of 3D structure
When certain assumptions hold, we can recover structure from a single view
In general, we need multi-view geometry
Image source
But first, we need to understand the geometry of a single camera…

## Slide 9: Camera calibration
Normalized (camera) coordinate system: camera center is at the origin, the principal axis is the z-axis, x and y axes of the image plane are parallel to x and y axes of the world
Camera calibration: figuring out transformation from world coordinate system to image coordinate system
world coordinate system

## Slide 10: Review: Pinhole camera model

## Slide 11: Principal point
Principal point (p): point where principal axis intersects the image plane
Normalized coordinate system: origin of the image is at the principal point
Image coordinate system: origin is in the corner

## Slide 12: Principal point offset
We want the principal point to map to (px, py) instead of (0,0)
px
py

## Slide 13: Principal point offset
principal point:
px
py

## Slide 14: Principal point offset
calibration matrix K
principal point:
px
py
projection matrix [I | 0]

## Slide 15: Pixel coordinates
mx pixels per meter in horizontal direction, my pixels per meter in vertical direction
Pixel size:
pixels/m
m
pixels
Notes: To convert from metric image coordinates to pixel coordinates, we have to multiply the x, y coordinates by the x, y pixel magnification factors (pix/m)
Beta_x, beta_y is the principal point coordinates in pixels

## Slide 16: Camera rotation and translation
In general, the camera coordinate frame will be related to the world coordinate frame by a rotation and a translation
coords. of point in camera frame
coords. of camera center in world frame
coords. of a point in world frame
Conversion from world to camera coordinate system (in non-homogeneous coordinates):
camera coordinate system
world coordinate system

## Slide 17: Camera rotation and translation
3D transformation matrix (4 x 4)

## Slide 18: Camera rotation and translation
3D transformation matrix (4 x 4)

## Slide 19: Camera rotation and translation
3D transformation matrix (4 x 4)
perspective projection matrix (3 x 4)
2D transformation matrix (3 x 3)

## Slide 20: Camera rotation and translation

## Slide 21: Camera rotation and translation

## Slide 22: Camera parameters
Intrinsic parameters
  Principal point coordinates
  Focal length
  Pixel magnification factors
  Skew (non-rectangular pixels)
  Radial distortion

## Slide 23: Camera parameters
Intrinsic parameters
  Principal point coordinates
  Focal length
  Pixel magnification factors
  Skew (non-rectangular pixels)
  Radial distortion
Extrinsic parameters
  Rotation and translation relative to world coordinate system
  What is the projection of the camera center?
coords. of camera center in world frame
The camera center is the null space of the projection matrix!

## Slide 24: Camera calibration

## Slide 25: Camera calibration
Given n points with known 3D coordinates Xi and known image projections xi, estimate the camera parameters
Xi
xi

## Slide 26: Camera calibration: Linear method
Two linearly independent equations

## Slide 27: Camera calibration: Linear method
P has 11 degrees of freedom
One 2D/3D correspondence gives us two linearly independent equations
  6 correspondences needed for a minimal solution
Homogeneous least squares: find p minimizing ||Ap||2
  Solution given by eigenvector of ATA with smallest eigenvalue

## Slide 28: Camera calibration: Linear method
Note: for coplanar points that satisfy ΠTX=0, we will get degenerate solutions (Π,0,0), (0,Π,0), or (0,0,Π)

## Slide 29: Camera calibration: Linear vs. nonlinear
Linear calibration is easy to formulate and solve, but it doesn’t directly tell us the camera parameters
In practice, non-linear methods are preferred
  Write down objective function in terms of intrinsic and extrinsic parameters
  Define error as sum of squared distances between measured 2D points and estimated projections of 3D points
  Minimize error using Newton’s method or other non-linear optimization
  Can model radial distortion and impose constraints such as known focal length and orthogonality
vs.

## Slide 30: Homography Example
Camera Center
Slide from A. Efros, S. Seitz, D. Hoiem

## Slide 31: Problem set-up
x = K [R t] X
x' = K' [R' t'] X
t=t'=0
x'=Hx where H = K' R' R-1 K-1
Typically only R and f will change (4 parameters), but, in general, H has 8 parameters
f
f'
.
x
x'
X

## Slide 32: A taste of multi-view geometry: Triangulation
Given projections of a 3D point in two or more images (with known camera matrices), find the coordinates of the point

## Slide 33: Triangulation
Given projections of a 3D point in two or more images (with known camera matrices), find the coordinates of the point
O1
O2
x1
x2
X?

## Slide 34: Triangulation
We want to intersect the two visual rays corresponding to x1 and x2, but because of noise and numerical errors, they don’t meet exactly
O1
O2
x1
x2
X?

## Slide 35: Triangulation: Geometric approach
Find shortest segment connecting the two viewing rays and let X be the midpoint of that segment
O1
O2
x1
x2
X

## Slide 36: Triangulation: Nonlinear approach
Find X that minimizes
O1
O2
x1
x2
X?
P1X
P2X

## Slide 37: Triangulation: Linear approach
Cross product as matrix multiplication:

## Slide 38: Triangulation: Linear approach
Two independent equations each in terms of three unknown entries of X

## Slide 39: Camera calibration revisited
What if world coordinates of reference 3D points are not known?
We can use scene features such as vanishing points
Slide from Efros, Photo from Criminisi

## Slide 40: Camera calibration revisited
What if world coordinates of reference 3D points are not known?
We can use scene features such as vanishing points
Vanishing
point
Vanishing
line
Vanishing
point
Vertical vanishing
point
(at infinity)
Slide from Efros, Photo from Criminisi

## Slide 41: Recall: Homogenous Coordinates
Points
Lines
Lines passing through 2 points
Intersection of 2 lines
Points at infinity
Intersection of 2 parallel lines?

## Slide 42: Recall: Homogenous Coordinates
Points
Lines
Lines passing through 2 points
Intersection of 2 lines
Points at infinity
Intersection of 2 parallel lines?

## Slide 43: Recall: Vanishing points
image plane
line in the scene
vanishing point v
All lines having the same direction share the same vanishing point
camera
center

## Slide 44: Computing vanishing points
X∞ is a point at infinity, v is its projection: v = PX∞
The vanishing point depends only on line direction
All lines having direction d intersect at X∞
v
X0
Xt

## Slide 45: Calibration from vanishing points
Consider a scene with three orthogonal vanishing directions:
Note: v1, v2 are finite vanishing points and v3 is an infinite vanishing point
v2
v1
.
v3
.
Notes: The third homogeneous coordinate of an infinite vanishing point is 0. Infinite vanishing points correspond to directions of lines that are parallel to the image plane.

## Slide 46: Calibration from vanishing points
Consider a scene with three orthogonal vanishing directions:
We can align the world coordinate system with these directions
v2
v1
.
v3
.

## Slide 47: Calibration from vanishing points
p1 = P(1,0,0,0)T – the vanishing point in the x direction
Similarly, p2 and p3 are the vanishing points in the y and z directions
p4 = P(0,0,0,1)T – projection of the origin of the world coordinate system
Problem: we can only know the four columns up to independent scale factors, additional constraints needed to solve for them

## Slide 48: Calibration from vanishing points
Let us align the world coordinate system with three orthogonal vanishing directions in the scene:

## Slide 49: Calibration from vanishing points
Let us align the world coordinate system with three orthogonal vanishing directions in the scene:
Orthogonality constraint:

## Slide 50: Calibration from vanishing points
Let us align the world coordinate system with three orthogonal vanishing directions in the scene:
Orthogonality constraint:
Rotation disappears, each pair of vanishing points gives constraint on focal length and principal point

## Slide 51: Calibration from vanishing points
Can solve for focal length, principal point
Cannot recover focal length, principal point is the third vanishing point

## Slide 52: Rotation from vanishing points
Constraints on vanishing points:
After solving for the calibration matrix:
Notice:
Thus,
Get λi by using the constraint ||ri||2 = 1.

## Slide 53: Calibration from vanishing points: Summary
Solve for K (focal length, principal point) using three orthogonal vanishing points
Get rotation directly from vanishing points once calibration matrix is known
Advantages
  No need for calibration chart, 2D-3D correspondences
  Could be completely automatic
Disadvantages
  Only applies to certain kinds of scenes
  Inaccuracies in computation of vanishing points
  Problems due to infinite vanishing points

## Slide 54: Application: Single View Reconstruction
Piero della Francesca, Flagellation, ca. 1455
A. Criminisi, M. Kemp, and A. Zisserman,Bringing Pictorial Space to Life: computer techniques for the analysis of paintings, Proc. Computers and the History of Art, 2002
Find heights (Hint: estimate horizon)
Find location on ground
Find pattern of the ground (Hint: homography)

## Slide 55: Application: Single View Reconstruction
Are the heights of the two groups of people consistent with one another?
  Measure heights using Christ as reference
Piero della Francesca, Flagellation, ca. 1455
A. Criminisi, M. Kemp, and A. Zisserman,Bringing Pictorial Space to Life: computer techniques for the analysis of paintings, Proc. Computers and the History of Art, 2002

## Slide 56: Application: 3D modeling from a single image
A. Criminisi, M. Kemp, and A. Zisserman,Bringing Pictorial Space to Life: computer techniques for the analysis of paintings, Proc. Computers and the History of Art, 2002

## Slide 57: Measurements on planes
1
2
3
4
1
2
3
4
Approach: unwarp then measure
What kind of warp is this?
Notes: homography!

## Slide 58: Image rectification
To unwarp (rectify) an image
solve for homography H given p and p′
how many points are necessary to solve for H?
p
p′

## Slide 59: Image rectification: example
Piero della Francesca, Flagellation, ca. 1455

## Slide 60: Application: 3D modeling from a single image
J. Vermeer, Music Lesson, 1662
A. Criminisi, M. Kemp, and A. Zisserman,Bringing Pictorial Space to Life: computer techniques for the analysis of paintings, Proc. Computers and the History of Art, 2002

## Slide 61: Application: Fully automatic modeling
D. Hoiem, A.A. Efros, and M. Hebert, Automatic Photo Pop-up, SIGGRAPH 2005.
http://dhoiem.cs.illinois.edu/projects/popup/popup_movie_450_250.mp4
sky
vertical
ground

## Slide 62: Application: Object detection
D. Hoiem, A.A. Efros, and M. Hebert, Putting Objects in Perspective, CVPR 2006

## Slide 63: Application: Image editing
Inserting synthetic objects into images: http://vimeo.com/28962540
K. Karsch and V. Hedau and D. Forsyth and D. Hoiem, Rendering Synthetic Objects into Legacy Photographs, SIGGRAPH Asia 2011

## Slide 64: Preview: Structure from motion
Camera 3
R3,t3
Figure credit: Noah Snavely
Camera 1
Camera 2
R1,t1
R2,t2
Given 2D point correspondences between multiple images, compute the camera parameters and the 3D points
Notes: Structure from motion solves the following problem:
Given a set of images of a static scene with 2D points in correspondence, shown here as color-coded points, find…
a set of 3D points P and
a rotation R and position t of the cameras that explain the observed correspondences. In other words, when we project a point into any of the cameras, the reprojection error between the projected and observed 2D points is low.
This problem can be formulated as an optimization problem where we want to find the rotations R, positions t, and 3D point locations P that minimize sum of squared reprojection errors f. This is a non-linear least squares problem and can be solved with algorithms such as Levenberg-Marquart. However, because the problem is non-linear, it can be susceptible to local minima. Therefore, it’s important to initialize the parameters of the system carefully. In addition, we need to be able to deal with erroneous correspondences.

## Slide 65: Preview: Structure from motion
Camera 3
R3,t3
Camera 1
Camera 2
R1,t1
R2,t2
Structure: Given known cameras and projections of the same 3D point in two or more images, compute the 3D coordinates of that point
  Triangulation!
?
Notes: Structure from motion solves the following problem:
Given a set of images of a static scene with 2D points in correspondence, shown here as color-coded points, find…
a set of 3D points P and
a rotation R and position t of the cameras that explain the observed correspondences. In other words, when we project a point into any of the cameras, the reprojection error between the projected and observed 2D points is low.
This problem can be formulated as an optimization problem where we want to find the rotations R, positions t, and 3D point locations P that minimize sum of squared reprojection errors f. This is a non-linear least squares problem and can be solved with algorithms such as Levenberg-Marquart. However, because the problem is non-linear, it can be susceptible to local minima. Therefore, it’s important to initialize the parameters of the system carefully. In addition, we need to be able to deal with erroneous correspondences.

## Slide 66: Preview: Structure from motion
Camera 3
R3,t3
Camera 1
Camera 2
R1,t1
R2,t2
Motion: Given a set of known 3D points seen by a camera, compute the camera parameters
  Calibration!
?
?
?
Notes: Structure from motion solves the following problem:
Given a set of images of a static scene with 2D points in correspondence, shown here as color-coded points, find…
a set of 3D points P and
a rotation R and position t of the cameras that explain the observed correspondences. In other words, when we project a point into any of the cameras, the reprojection error between the projected and observed 2D points is low.
This problem can be formulated as an optimization problem where we want to find the rotations R, positions t, and 3D point locations P that minimize sum of squared reprojection errors f. This is a non-linear least squares problem and can be solved with algorithms such as Levenberg-Marquart. However, because the problem is non-linear, it can be susceptible to local minima. Therefore, it’s important to initialize the parameters of the system carefully. In addition, we need to be able to deal with erroneous correspondences.

## Slide 67: Useful reference