## Slide 1: Filtering (in Frequency Domain)
While we wait,
Who do you see in this picture?
Many slides from Derek Hoiem.
CS 543 / ECE 549 – Saurabh Gupta
A. Albert Einstein
B. Marilyn Monroe
C. None of these

## Slide 2: Today’s Class
Fourier transforms
Filtering in frequency domain
Sampling
Image Pyramids

## Slide 3: Why does the Gaussian give a nice smooth image, but the square filter give edgy artifacts?
Gaussian
Box filter
Notes: Things we can’t understand without thinking in frequency

## Slide 4: Thinking in terms of frequency

## Slide 5: Jean Baptiste Joseph Fourier (1768-1830)
had crazy idea (1807):
Any univariate function can be rewritten as a weighted sum of sines and cosines of different frequencies.
Don’t believe it?
  Neither did Lagrange, Laplace, Poisson and other big wigs
  Not translated into English until 1878!
But it’s (mostly) true!
  called Fourier Series
  there are some subtle restrictions
...the manner in which the author arrives at these equations is not exempt of difficulties and...his analysis to integrate them still leaves something to be desired on the score of generality and even rigour.
Laplace
Lagrange
Legendre
Slides: Efros
Notes: Fourier also discovered the “greenhouse effect”

## Slide 6: A sum of sines
Our building block:
Add enough of them to get any signal f(x) you want!

## Slide 7: Frequency Spectra
Square Wave:
Fourier Transform:

## Slide 8
1 Term
2nd Term
2 Terms
2 Terms
3rd Term
3 Terms

## Slide 9
101 Terms
31 Terms
15 Terms

## Slide 11: Fourier Transform
Fourier transform stores the magnitude and phase at each frequency
  Magnitude encodes how much signal there is at a particular frequency
  Phase encodes spatial information (indirectly)
  For mathematical convenience, this is often notated in terms of complex numbers
Amplitude:
Phase:

## Slide 12: Computing the Fourier Transform
Continuous:
Discrete:
Euler’s Formula:

## Slide 13: Properties of Fourier Transforms
Linearity:
Fourier transform of a real signal is symmetric about the origin
The energy of the signal is the same as the energy of its Fourier transform
See Szeliski Book (3.4)

## Slide 14: The Convolution Theorem
The Fourier transform of the convolution of two functions is the product of their Fourier transforms
The inverse Fourier transform of the product of two Fourier transforms is the convolution of the two inverse Fourier transforms
Convolution in spatial domain is equivalent to multiplication in frequency domain!

## Slide 15: Other signals
We can also think of all kinds of other signals the same way
xkcd.com

## Slide 16: Images
Strong horizontal gradients
Strong vertical gradients
Low frequencies
Diagonal Frequencies

## Slide 17: Fourier analysis in images
Intensity Image
Fourier Image
http://sharp.bu.edu/~slehar/fourier/fourier.html#filtering

## Slide 18: Signals can be composed
+
=
http://sharp.bu.edu/~slehar/fourier/fourier.html#filtering
More: http://www.cs.unm.edu/~brayer/vision/fourier.html

## Slide 19: Filtering in spatial domain
1
0
-1
2
0
-2
1
0
-1
*
=

## Slide 20: Filtering in frequency domain
FFT
FFT
Inverse FFT
=

## Slide 21: Why does the Gaussian give a nice smooth image, but the square filter give edgy artifacts?
Gaussian
Box filter
Notes: Things we can’t understand without thinking in frequency

## Slide 22: Filtering in frequency domain (Box)
FFT
FFT
Inverse FFT
=

## Slide 23: Filtering in frequency domain (Gaussian)
FFT
FFT
Inverse FFT
=

## Slide 24: Filtering in frequency domain (Gaussian)
Spatial Domain
Frequency Domain

## Slide 25: Filtering in frequency domain (Gaussian)

## Slide 26: Filtering in frequency domain (Gaussian)

## Slide 27: Sampling
Why does a lower resolution image still make sense to us? What do we lose?
Image: http://www.flickr.com/photos/igorms/136916757/

## Slide 28
Throw away every other row and column to create a 1/2 size image
Subsampling by a factor of 2

## Slide 29: Aliasing problem
1D example (sinewave):
Source: S. Marschner

## Slide 30: Aliasing problem
Source: S. Marschner
1D example (sinewave):

## Slide 31: Aliasing problem
Sub-sampling may be dangerous….
Characteristic errors may appear:
  “Wagon wheels rolling the wrong way in movies” See
  “Checkerboards disintegrate in ray tracing”
  “Striped shirts look funny on color television”
Source: D. Forsyth

## Slide 32: Aliasing in video
Slide by Steve Seitz

## Slide 33: Aliasing in graphics
Source: A. Efros

## Slide 34: Sampling and aliasing
Slide from Derek Hoiem.

## Slide 35: Aliasing in Frequency Domain
Source: Forsyth and Ponce
No Aliasing
Aliasing

## Slide 36: Nyquist-Shannon Sampling Theorem
When sampling a signal at discrete intervals, the sampling frequency must be  2  fmax
fmax = max frequency of the input signal
This will allows to reconstruct the original perfectly from the sampled version
good
bad
v
v
v
Slide from Derek Hoiem.

## Slide 37: Anti-aliasing
Solutions:
Sample more often
Get rid of all frequencies that are greater than half the new sampling frequency
  Will lose information
  But it’s better than aliasing
  Apply a smoothing filter
Slide from Derek Hoiem.

## Slide 38: Algorithm for downsampling by factor of 2
Start with image(h, w)
Apply low-pass filter
Sample every other pixel
Slide from Derek Hoiem.

## Slide 39: Anti-aliasing
Forsyth and Ponce 2002

## Slide 40: Subsampling without pre-filtering
1/4 (2x zoom)
1/8 (4x zoom)
1/2
Slide by Steve Seitz

## Slide 41: Subsampling with Gaussian pre-filtering
G 1/4
G 1/8
Gaussian 1/2
Slide by Steve Seitz

## Slide 42: Gaussian pyramid (Repeated blurring and sampling)
Source: Forsyth

## Slide 43: Laplacian pyramid
Source: Forsyth

## Slide 44: Creating the Difference of Gaussian Pyramid
Downsample (Smooth(G1))
Smooth
(Upsample(G2))
Image = G1
L1
G2
G4
L2
L3
Use same filter for smoothing in each step (e.g., Gaussian with )
Downsample/upsample with “nearest” interpolation
Downsample (Smooth(G2))
Smooth, then downsample
G3
G1
Smooth
(Upsample(G3))
Smooth
(Upsample(G4))
G2
G3
-
-
-
Leopard, Elephant image from Olivia and Torralba

## Slide 45: Creating the Difference of Gaussian Pyramid
Downsample (Smooth(G1))
Smooth
(Upsample(G2))
Image = G1
L1
G2
G4
L2
L3
G3
Use same filter for smoothing in each step (e.g., Gaussian with )
Downsample/upsample with “nearest” interpolation
Downsample (Smooth(G2))
Smooth, then downsample
G3
G1
Smooth
(Upsample(G3))
Smooth
(Upsample(G4))
G2
G3
-
-
-
Spatial Response

## Slide 46: Creating the Difference of Gaussian Pyramid
Downsample (Smooth(G1))
Smooth
(Upsample(G2))
Image = G1
L1
G2
G4
L2
L3
G3
Use same filter for smoothing in each step (e.g., Gaussian with )
Downsample/upsample with “nearest” interpolation
Downsample (Smooth(G2))
Smooth, then downsample
G3
G1
Smooth
(Upsample(G3))
Smooth
(Upsample(G4))
G2
G3
-
-
-
Frequency Response

## Slide 47: Creating the Difference of Gaussian Pyramid
Downsample (Smooth(G1))
Smooth
(Upsample(G2))
Image = G1
L1
G2
G4
L2
L3
G3
Can also use Smooth(G1), but then reverse isn’t the exact same.
Technically, this is a Difference of Gaussian pyramid and not a Laplacian pyramid.
Downsample (Smooth(G2))
Smooth, then downsample
G3
G1
Smooth
(Upsample(G3))
Smooth
(Upsample(G4))
G2
G3
-
-
-

## Slide 48: Laplacian filter
Gaussian
unit impulse
Laplacian of Gaussian
Source: Lazebnik

## Slide 49: Images in a Difference of Gaussian Pyramid

## Slide 50
Dali: “Gala Contemplating the Mediterranean Sea” (1976)

## Slide 51
Dali: “Gala Contemplating the Mediterranean Sea” (1976)
Images in a Difference of Gaussian Pyramid

## Slide 52: Reconstructing from Diff of Gauss Pyramid
Image = G1
L1
G2
G4
L2
L3
G3
G3 = L3 + Smooth(Upsample(G4))
G2 = L2 + Smooth(Upsample(G3))
G1 = L1 + Smooth(Upsample(G2))
Use same filter for smoothing as in deconstruction
Upsample with “nearest” interpolation
Reconstruction will be nearly lossless

## Slide 53: Application: Image Blending
Laplacian pyramid blending (Burt and Adelson 1983b)

## Slide 54: Blending

## Slide 55: Alpha Blending / Feathering
0
1
0
1
+
=
Iblend = aIleft + (1-a)Iright

## Slide 56: Affect of Window Size
0
1
left
right
0
1

## Slide 57: Affect of Window Size
0
1
0
1

## Slide 58: Good Window Size
0
1
“Optimal” Window: smooth but not ghosted

## Slide 59: What is the Optimal Window?
To avoid seams
  window = size of largest prominent feature
To avoid ghosting
  window <= 2*size of smallest prominent feature
Natural to cast this in the Fourier domain
  largest frequency <= 2*size of smallest frequency
  image frequency content should occupy one “octave” (power of two)
FFT

## Slide 60: What if the Frequency Spread is Wide
Idea (Burt and Adelson)
  Compute Fleft = FFT(Ileft), Fright = FFT(Iright)
  Decompose Fourier image into octaves (bands)
    Fleft = Fleft1 + Fleft2 + …
  Feather corresponding octaves Flefti with Frighti
    Can compute inverse FFT and feather in spatial domain
  Sum feathered octave images in frequency domain
Better implemented in spatial domain
FFT

## Slide 61: Octaves in the Spatial Domain
Bandpass Images
Lowpass Images

## Slide 62: Pyramid Blending
0
1
0
1
0
1
Left pyramid
Right pyramid
blend

## Slide 63: Pyramid Blending

## Slide 64
laplacian
level
4
laplacian
level
2
laplacian
level
0
left pyramid
right pyramid
blended pyramid

## Slide 65: Blending Regions

## Slide 66: Laplacian Pyramid: Blending
General Approach:
  Build Laplacian pyramids LA and LB from images A and B
  Build a Gaussian pyramid GR from selected region R
  Form a combined pyramid LS from LA and LB using nodes of GR as weights:
    LS(i,j) = GR(I,j,)*LA(I,j) + (1-GR(I,j))*LB(I,j)
  Collapse the LS pyramid to get the final blended image

## Slide 67: Major uses of image pyramids
Compression
Object detection
  Scale search
  Features
Detecting stable interest points
Registration
  Course-to-fine

## Slide 68: Recap
Sometimes it makes sense to think of filtering in the frequency domain
  Fourier analysis
Sampling and Aliasing
Image Pyramids